| Temperature Data Logger EBI-125 A-EM-500-F1,6-2K |
| --- |
|  | Technical Data Meauring range -40 ... +125°C +135°C up to max. 3 h +140°C up to max. 1 h Accuracy ±0.3°C Measuring probe Pt1000, internal Probe length 500 mm, diameter 3 mm Resolution 0.1°C Measuring rate from 1s ... 8 h Memory 18.000 readings (2 channels, 9.000 readings per channel) Battery 3.6 V Lithium Measuring mode endless, Start/Stop or start with predetermined measuring rate Interface M-BUS, readout with Interface EBI-KSY-AE2000, EBI-AE-S Vers. C Battery life approx. 3 to 5 years (depending on measuring rate) Dimensions Ø 48 mm x 28 mm Weight 150 g Protection class IP 68 Certificates 3 point factory calibration according to DIN ISO 9001 Product-No 1340-2139 |
| Attributes |
| High accuracy Programming and evaluation with PC Completely waterproof According to EN 15883 According to DIN EN 285, 554, DIN 58946-6 Temperature resistant up to +140°C Factory calibration certificate Stainless steel housing, safe for food products Small dimensions Different forms No wiring necessary 2 measuring probes, probe diameter 1.5mm Probe length 500mm |