| Temperature Pressure Logger EBI-125 A-PT-AK-5 N for Steam Sterilizers |
| --- |
|  | Technical Data Type Pressure Temperature Memory 9.000 readings 9.000 readings Measuring range 0 ... 4 bar (burst pressure 10 bar) -40 ... +140°C (+140°C up to max. 1 hour 1 h) Accuracy ±0,5% of measuring range ±0,3°C Resolution 1 mbar 0.1°C Measuring probe ceramic sensor Pt 1000 Needle length 40 mm, diameter 3 mm, blunt Pressure resistance housing 0 bar ... 10 bar Measuring rate selectable from 1s ... 8 h Measuring mode endless, Start/Stop, Start with predetermined measuring rate Battery life aprox. 1-3 years (depending on measuring rate) Dimensions Ø 48 mm x 28 mm Weight 200 g Protection class IP 68 Certificate 6 points according to DIN ISO 9001 Product-No 1340-2132 |
| Applications |
| Monitoring applications in chemical an pharmaceutical industry Monitors temperature and pressure in autoclaves Monitors pressure tests in heating systems |
| Attributes |
| Programming and evaluation with PC Waterproof High accuracy Stainless steel housing Factory calibration certificate Long sensor life due to acid and base resistant ceramic sensor Compact Light weight Easy handling Approved according to EN 554 und 285 |