| Temperature Data Logger EBI-6 |
| --- |
|  | Technical Data Measuring range -30 to +50°C Measuring accuracy ±0.8°C Resolution 0.1°C Measuring rate from 60s to 24h Memory 4.000 values Measuring mode automatic with endless, Start/Stop or start with set measuring rate Battery life up to 2 years (at measuring rate of 15 minutes) Battery replacement by user Logger-housing Plastic suitable for food products Protection class IP 67 Start / Stop with buttons Calibration certificate according to ISO possible against surcharge Product-No 1600-0000 |
| Applications |
| Temperature monitoring during transport Temperature chamber monitoring Cooling chamber monitoring Storage monitoring |
| Attributes |
| Compact and handy Waterproof IP 67 Optical Alarm Replaceable battery Evaluation software Good price/performance ratio |