| Humidity/Temperature Logger EBI-2-TH-611 (with internal Sensor) |
| --- |
|  | Technical Data Humidity (channel 1) Temperature (channel 2) Measuring range 0 to 100% rH -40 to +75°C Measuring accuracy ±2% rH ± 1 Digit (-10 to +50°C and 5 to 95% rH) ±0.3°C ± 1 Digit Resolution 0.1% rH 0.1°C Memory 30.000 values 30.000 values Display function -20 to +50°C -20 to +50°C Operating temperature -40 to +75°C -40 to +75°C Storage temperature -40 to +75°C -40 to +75°C Measuring rate selectable from 1 s to 8 h selectable from 1 s to 8 h Measuring mode endless, Start/Stop, Start with set measuring rate endlesss, Start/Stop, Start with set measuring rate Battery 3,6 V Lithium 3,6 V Lithium Battery life approx. 3 to 5 years approx. 3 to 5 years Dimensions 96 mm x 48 mm x 28 mm 96 mm x 48 mm x 28 mm Weight 100 g 100 g Certificate 3 point factory calibration certificate 3 point factory calibratin certificate Product-No 1613-1303 |
| Applications |
| Temperature and humidity monitoring Transport monitoring Climate control Storage Computer rooms |
| Attributes |
| High accuracy Also available with external probes Programming and evaluation with PC Current values shown on display Factory calibration certificate |