| Temperature- and pH-Logger EBI 30-pH (Set) with Interface and Software |
| --- |
|  | Technical Data Type EBI 30-pH Measuring probe temperature Pt 1000 Measuring range temperature 0 ... 100°C Resolution temperature 0.01°C Accuracy Temperature ±0.2°C Measuring range pH 1 ... 14 pH Resolution 0.01 pH Accuracy ±0,2 pH Housing Stainless steel V4A Dimensions Length 400 mm / Diameter 25 mm Weight 700 g Memory 16.000 readings per channel Measuring rate 1s - 24h Protection class IP 68 Battery Lithium, exchangeable Interface USB Product-No 1340-6300 |
| Applications |
| Measure pH-value and temperature Industrial water, waste water Liquids Food production Validation of washer-disinfectors according to EN 15883 Routine checks of washer-disinfectors Monitor pH-Value, temperature and time directly during process |
| Attributes |
| Waterproof High accuracy Temperature resistant up to 100°C Fast data transfer Progamming and evaluation with PC Starter-Set consists of: Data logger Interface Software |