| Truck Logger EBI-2T-511 (ATP-approved) |
| --- |
|  | Technical Data Type Standard-LKW-System Universal-LKW-System Measuring range -40 to +75°C -40 to +75°C Measuring accuracy ±0.2°C ± 1 Digit ±0.3°C ± 1 Digit Resolution 0.1°C 0.1°C Display LCD LCD Probes Pt 1000-Sensor, internal Pt 1000-probe external Number of probes 1 1, 2 or 4 Memory 40.000 samples to 240.000 samples Measuring interval 1 s to 8 h, freely programmable (15 minutes recommended for transport) 1 s bis 8 h, freely programmable (15 minutes recommended for transport Interface RS 232 RS 232 Protection class IP 65 when protective cap is on RS 232-interface IP 65 when top of protective case is closed Certificate 3 point factory calibration 3 point factory calibration Product-No 1621-1013 |
| Applications |
| Temperature monitoring Storage Transport |
| Attributes |
| ATP-approved Can be used anywhere Logger is programmed and evaluated with PC Standard system requires no wiring Factory calibration certificate Universal system can monitor up to 4 measuring points in cargo area |