| Data Logger with External Probe EBI-125 A-E-OF |
| --- |
|  | Technical Data Measuring range -40 to +400°C Measuring accuracy ±0.3°C Resolution 0.1°C Sensor Pt1000, pointed, diameter 1,5 or 3mm, L2-external sensor Measuring rate from 1 s to 8 h Memory 18.000 readings Measuring mode endless, Start/Stop Battery 3.6 V Lithium Battery life 3 to 5 years Housing stainless steel, PEEK Dimensions Ø 48 x 28 mm high Protection class IP 68 Weight approx. 150 g Certificate 3 point factory calibration Interface Interface EBI-KSY-AE 2000 Product-No 1340-1918 |
| Attributes |
| Completely waterproof Temperature resistant up to +140°C Stainless steel housing, suitable for food products Small dimensions High accuracy Factory calibration certificate Different forms No wires necesary Different probes available Programming and evalution with PC |