| Temperature/Pressure Data Logger EBI-125 A-PT with flexible probes |
| --- |
|  | Technical Data Type Pressure Temperature Memory 6.000 readings 2 x 6.000 readings Measuring range 0 ... 4 bar (Burst pressure 10 bar) -40 ... +150°C (+150°C up to max. 1 h) Accuracy ±0,5% of measuring range ±0.1°C ± 1 Digit Resolution 1 mbar 0.1°C Measuring probe ceramic pressure sensor 2 x Pt 1000, Ø 1,5 mm Probe length 2 flexible probes, 500 mm each, diameter 1,5 mm Pressure resistance of housing 0 bar ... 10 bar Measuring rate selectable from 1s ... 8 h Measuring mode endless, Start/Stop, Start with predetermined measuring rate Battery life approx. 1-3 years (depending on measuring rate) Dimensions Ø 48 mm x 28 mm Weight 200 g Protection class IP 68 Certificate 9 points according to DIN ISO 9001 Product-No 1340-2136 |
| Applications |
| Monitors temperature and pressure in chemical/pharmaceutical industry Monitors temperature and pressure in autoclaves Controls pressure in heating systems |
| Attributes |
| Programming and evaluation with PC Waterproof High accuracy According to EN 285/554, DIN 58946-6 and DIN EN 13060 Factory calibration certificate |