| Temperature Data Logger EBI-125 A |
| --- |
|  | Technical Data Sensor Pt1000, internal Measuring range -40 ... +125°C +135°C up to max. 3 h +140°C up to max. 1 h Accuracy ±0.3°C Resolution 0.1°C Measuring rate from 1s ... 8 h Memory 18.000 readings Battery 3,6 V Lithium Measuring mode endlesss, Start/Stop or Start with predermined measuring rate Interface Interface EBI-KSY-AE2000 Batteriy life approx. 3 to 5 years (according to measuring rate) Dimensions Ø48 mm x 28 mm Weight 150 g Protection class IP 68 Certificate 3 point factory calibration Product-No 1340-1916 |
| Attributes |
| Completely waterproof Temperature resistant up to +140°C Stainless steel, PEEK, safe for food products Small dimensions High accuracy Factory calibration certificate Different forms No wiring necessary |