| Temperature Data Logger EBI-125 A-EM-250-F1,6 with flexible probe |
| --- |
|  | Technical Data Measuring range -40 to +125°C up to +140°C max. 1 h up to +135°C max. 3 h Accuracy ±0.3°C Resolution 0.1°C Sensor Pt1000 Needle length 250 mm, diameter 1,5 mm Measuring rate from 1 s to 8 h Memory 18.000 readings Measuring modus endless, Start/Stop Battery 3.6 V Lithium Battery life 3 t 5 years Housing material stainless steel, PEEK Dimensions Ø 48 x 28 mm high Protection class IP 68 Weight ca. 150 g Certificate 3 point factory calibration Interface Interface EBI-KSY-AE 2000 Product-No 1340-2146 |
| Attributes |
| Completely waterproof Temperture resistant up to +140°C Stainless steel housing, suitable for food products Small dimensions High accuracy Factory calibration certificate Different forms No wiring necessary Stainless steel probe, blunt External sensor Programming and evaluation with PC According to EN 285, 554, DIN 58946-6 Probe ø 1.5mm Probe length 250mm |