| Precision-Temperature Logger Pt 1000 EBI-2T-Series 300 EBI-2T-311 EBI-2T 312 EBI-2T-313 |
| --- |
|  | Technical Data Number of channels 1, 2 or 4 Memory up to 60.000 values Measuring range -50 up to +150°C/400°C Measuring accuracy ±0.4°C ± 1 Digit Resolution 0.1°C Display function Housing temperature -20 bis +50°C Measuring rate Ca be selected from 1s to 8 h Measuring mode endless, Start/Stop Battery 3,6 V Lithium Battery life approx. 5 to 8 years Dimensions 96 x 48 x 28 mm Weight 100 g Protection class IP 40 Certificate 3 point factory calibration Sensor external Product-No 1641-1214 |
| Versions EBI-2T-Series 300 |
| Temperature logger for 1 ext. probe EBI-2T-311 Part No. 1641-1214 Temperature logger for 2 ext. probes EBI-2T-312 Part No. 1641-1423 Temperature logger for 4 ext. probes EBI-2T-313 Part No. 1641-1834 |
| Applications |
| Record temperature values for air, fluids and ductile substances Cooling chambers and freezers Cooling cabinets Process monitoring Transport monitoring Glass-coated probes for aggressive media Laboratories |
| Eigenschaften |
| High accuracy Different probes available Programming and evalutation with PC Current values shown on display Factory calibration certificate |