| Low-Cost-Thermometer TDC 100-N |
| --- |
|  | Technical Data Measuring range -40 to +150°C Resolution 0,1°C Accuracy ± 1.0°C in range +5 to +95°C Sensor NTC Needle type probe Stainless steel, Ø 4 mm, L=120 mm, pointed Thermal response time (t99) 19 s (water) Operating temperture 0 to +50°C Storage temperture -10 to +60°C Display 7 mm LCD Battery 1,5 V, G 10-A Dimensions 34 x 30 x 23 mm Weight approx. 13 g Protection class IP 40 Product-No 1340-1612 |
| Attributes |
| Fixed probe, pointed Robust and impact resistant Exchangeable battery °C/°F switchable Needle guard |